## Slide 1: Crypto-Engine on the Pi-5

## Slide 2: Pi 5 Cryptographic Support
Raspberry Pi 5 uses Arm Cortex-A76 cores
These cores on Pi-5 expose the Armv8-A Cryptographic Extensions:
AES
SHA-1/SHA-256
PMULL/PMULL2
Apps can use these directly via AArch64 intrinsics/assembly

## Slide 3: Block Diagram
Application
Intrinsics, Assembly or OS API
Cortex-A76 Core
Crypto Extension Unit
AES instructions
SHA1/SHA2 instr.
PMULL (GCM)

## Slide 4: Interface with the main processor
User space can interface with the processor through compiler intrinsics, assembly instructions, OS API calls or libraries like OpenSSL
Check CPU Features: grep -Eo 'aes|pmull|sha1|sha2' /proc/cpuinfo

## Slide 5: Examples: Rust Using Intrinsics
use core::arch::aarch64::{uint8x16_t, vaeseq_u8, vaesmcq_u8};
#[target_feature(enable = "aes,neon")] // Guarantees
unsafe fn aes_round(block: uint8x16_t, round_key: uint8x16_t) -> uint8x16_t {
let t = vaeseq_u8(block, round_key); // AESE instruction
vaesmcq_u8(t) // AESMC instruction
}
Function performs one AES round and returns the 128-bit state after one round
core::arch::aarch64 provides Rust intrinsics
target_feature() guarantees the function is only called on CPUs that support AES+NEON

## Slide 6: Examples: C++ Using OpenSSL
#include <openssl/evp.h>
#include <stdint.h>
int aes_gcm_encrypt(
const uint8_t *key32, const uint8_t *iv12,
const uint8_t *aad, int aad_len,
const uint8_t *pt, int pt_len,
uint8_t *ct, uint8_t tag[16])
{
EVP_CIPHER_CTX *c = EVP_CIPHER_CTX_new();
int out = 0, n;
EVP_EncryptInit_ex(c, EVP_aes_256_gcm(), NULL, NULL, NULL);
EVP_CIPHER_CTX_ctrl(c, EVP_CTRL_GCM_SET_IVLEN, 12, NULL);
EVP_EncryptInit_ex(c, NULL, NULL, key32, iv12);
if (aad_len) EVP_EncryptUpdate(c, NULL, &n, aad, aad_len);
EVP_EncryptUpdate(c, ct, &n, pt, pt_len); out += n;
EVP_EncryptFinal_ex(c, ct + out, &n); out += n;
EVP_CIPHER_CTX_ctrl(c, EVP_CTRL_GCM_GET_TAG, 16, tag);
EVP_CIPHER_CTX_free(c);
return out; // ciphertext length
}
OpenSSL EVP using aarch64 AES/PMULL assembly on Pi-5
Longer than intrinsics because of safety and portability
Needs to be linked with crypto.lib in build
Ex.
gcc -O3 aes_gcm.c -o aes_gcm -lcrypto