## Slide 1: Final Project By Aaron Tran, Melvin Contreras, Quinn BELL

## Slide 2: Inspiration
Streaming applications such as Discord, Skype, Messenger, Zoom, Teamspeak, etc.
  Ex. Discord Channel provides voice and audio calls
  Allows a Single user to send their voice and video to other members connected to the channel
  Every user can see each other’s voice/video
  Provide a secure alternative application
  (Fun Fact this project Idea was conceived over discord)

## Slide 3: Secure Pi-to-Pi AV Streaming (1 → 2)
Architecture: WebRTC mesh (one publisher → two subscribers)
  Publisher (Pi A): camera + mic → H.264 (video) + (audio) → Server-side application
  Signaling: Use TCP to exchange Keys including Rekeying
  Security: Elliptic Curve Diffie-Hellman (ECDH) encryption/decryption key exchange
  LAN friendly: On the same Network as the Server, no Server-side connection required
  Latency target: 150–250 ms E2E (Opus 20 ms frames, ptime=20, jitter 60–100 ms)
Pi D/PC (Server / SFU) Forwards Voice + Video
Pi A (Client) Publishes Cam+Mic
Pi B (Client) Publishes Cam+Mic
Pi C (Client) Publishes Cam+Mic

## Slide 4: Implementation Plan (Rust, Raspberry Pi 5)
Roles & Responsibilities
  Server (Pi D): Forwarder for H.264 (video) + Opus (audio). Handles rooms, RTCP (NACK/PLI), and bitrate guidance.
  Optional on server: recording and per-room stats. Potential Application
  Clients (Pis A/B/C): publish camera+mic; subscribe to room streams; UI controls (mute/PTT/video off).
Signaling & Security
  ECDH key exchange as well as rekeying
  Access control lists per room; join/leave events for presence.
Networking & QoS
  LAN-first: No Server Connection needed on same subnet; enable Server-side connection only for remote access.
  Audio priority: 24–48 kbps Opus, 20 ms frames; target 150–250 ms end-to-end.
  Start video 1–3 Mbps H.264 (hardware).
Deploy & Ops
  Run as system services on all Pis
  Central logs & basic metrics (CPU, jitter, bitrate) for quick diagnostics.
  Backup signaling config and room ACLs with tokens/certifications regularly.